## Slide 1: S3A/B STM L2 LAND products Product Performance Status
Pierre Féménias - ESA ESRIN
With contributions from the S3 Mission Performance Centre (S3 MPC)
S3 Mission Constellation Review #2 14 June 2021
VC

## Slide 2: S3-A&B STM Land Ice Product Performance
2
S3A
S3B
Ice Sheet Measurement Quality
Good measurement quality over ice sheet interior
Stable failure rate over mission (~11%) observed for both S3A/B satellites with expected high failure over the margins (areas of high slope).
S3A
Prototype Processing equivalent to Thematic Products in 2021
11.39% Failure
11.4% Failure
7.8% Failure
Land Ice Thematic Prototype shows 3.6% improvement in measurement quality over the Antarctic ice sheet, and 11% improvement over the margins.
Measurement Failure
0%
100%

## Slide 3: S3-A&B STM Land Ice Product Performance
3
Ice Sheet Precision over Low Slopes (Lake Vostok test site)
Over areas of low slope, mean S3A/B precision (measured using repeat elevation differences at orbit crossovers) is excellent at ~8cm (with expected seasonal variability)
Equivalent mean precision for CryoSat (LRM) is ~10cm
0.0m mean S3 difference indicates no polarization bias between ascending and descending tracks
S3A cycle 69
S3B cycle 51
Mean diff: 0.01 σ=0.07m
Mean diff: 0.00 σ=0.06m
Crossover Elevation Differences over Lake Vostok
PB2.68
Precision over whole S3A Mission
Precision over whole S3B Mission
10cm
10cm

## Slide 4: S3-A&B STM Land Ice Product Performance
4
Elevation Precision over the whole ice sheet measured per band of surface slope
S3A/B precision of elevation decreases with surface slope as expected.
At lower slopes (< 0.4∘), S3A has equal or better precision than CryoSat.
At high slopes CryoSat’s SARin mode has better performance as expected. Future S3 slope model improvements can reduce this difference.
Surface Slope of Greenland
S3A Precision per Slope Band

## Slide 5: S3-A&B STM Land Ice Product Performance
5
% of Crossovers < 1m (improved with new slope model in PB2.61)
50%
60%
PB2.61,2.68
A further slope model update is planned for 2021
S3AB Slope Correction
Nadir track
PB2.61,PB2.68

## Slide 6: S3-A&B STM Land Ice Product Performance
6
S3A/B Ice Sheet Measurement Accuracy measured by Airbourne Laser*
Slope Band | S3A - Airbourne Median Absolute Diff (m)
0.0 to 0.1° | 0.08
0.0 to 0.2° | 0.10
0.2 to 0.4° | 0.87
0.4 to 0.6° | 3.69
*Operation IceBridge
Accuracy at low slopes is excellent.
Accuracy reduces with slope as expected.

## Slide 7: S3-A&B STM Land Ice Product Performance
7
Surface elevation change of critical Antarctic and Greenland Glaciers is now being successfully measured by S3A and S3B.
After cross-calibration it is merged with CryoSat data in new ESA CCI ice sheet products to improve coverage and reduce uncertainty.
CS2
S3A

## Slide 8: S3-A&B STM Sea Ice Product Performance
8
S3A
S3B
Freeboard
Jan 2020
Jan 2020
S3A and S3B Arctic Freeboard
Near identical freeboard from S3A & S3B S3A& B have different ground tracks so minor differences expected.

## Slide 9: S3-A&B STM Sea Ice Product Performance
9
S3AB-CryoSat-2 Gridded Mean Freeboard
S3AB from PB2.68 have a higher distribution of mean freeboard compared to CS2, with larger differences near the coastline
Mean difference is 4cm

## Slide 10: S3-A&B STM Sea Ice Product Performance
10
S3AB Thematic Equivalent-CryoSat-2 Gridded Mean Freeboard
S3AB freeboard processed by GPOD with a configuration similar to the thematic S3 sea ice product has a near identical performance to CryoSat.
Mean difference is < 1cm.

## Slide 11: S3-A&B STM Sea Ice Product Performance
S3AB processed with thematic configuration tracks CS2 freeboard over Arctic winter season, whereas
current IPF freeboard has significant divergence