## Slide 1
S3 MPC S3 Performance over Sea Ice
Alan Muir1,2, David Brockley1 , Steve Baker1, Isobel Lawrence3
S3 Mission Performance Centre, ESL for Ice Surfaces
1Mullard Space Science Laboratory (MSSL), University College London (UCL), UK. 2 Centre for Polar Observation and Modeling (CPOM), UCL, UK.
3 University of Leeds (CPOM),UK
ESL STM Council Meeting #8 – Nov 2021

## Slide 2
Technical Note on Sea Ice Performance delivered on 22-Oct-21
  Details performance of latest operational products (PB2.68)
  Does not include future performance of Thematic products
  Baseline to measure against future products
S3 Sea Ice Performance

## Slide 3
S3 Freeboard Measurement Coverage
Using available L2 data from <= PB 2.68

## Slide 4
S3A
S3B
Mar 2020
Feb 2020
Jan 2020
Oct 2019
Nov 2019
Dec 2019
NSIDC Sea Ice 15% Extent
S3 Freeboard Coverage: Arctic Seasonal Variability
Passive Microwave

## Slide 5
Regional Freeboard Statistics
Winter 2019/2020
S3A
East Siberian Sea
Beaufort Sea
Hudson Bay
St John’s, Gulf of St Lawrence
Bering Sea
Central Arctic
E. Greenland Sea
Kara Sea
Canadian Islands
Laptev Sea
Monthly Number of S3A Freeboard Measurements per Arctic Basin
Chukchi Sea
Oct 2019
NSIDC Sea Ice Extent
Apr 2020
Notes: plot_fb_stats_multibasin.py -v nvals -m s3a -g -r nsidc

## Slide 6
Annual Arctic Sea Ice Extent (NSIDC) : 2016-2020
Aug 2020, Polarstern, photo: AWI
Melt Ponds in the Sea Ice
peak extent in mid-March

## Slide 7
Seasonal Arctic Freeboard Availability
S3A
Peak coverage Mid-March

## Slide 8
S3B
Seasonal Arctic Freeboard Availability
Peak coverage Mid-March

## Slide 9
2019
2020
2021
NSIDC
Maximum extent: October
Maximum coverage: August
Seasonal Antarctic Freeboard Availability
S3B
S3 maximum freeboard coverage lags maximum sea ice extent by ~2months

## Slide 10
S3A
S3B
S3A and S3B Freeboard Comparison
Freeboard (m)
Jan 2020

## Slide 11
Measurement Precision over Sea Ice
Using available L2 data from <= PB 2.68
?
?
Sea ice floe
Lead

## Slide 12
Mission | SLA SD over Leads | SLA SD over Floes
S3A | 12.5 | 11.4
CryoSat-2 | 4.1 | 9.8
Precision measured over very thin ice in Hudson Bay (as per Tilling et al) and compared with CS2
S3A lead SHA precision ~3x worse than CS2

## Slide 13
Poor Lead SHA Precision due to under-sampling of Specular Echoes

## Slide 14
 | No ZP | ZP2 | ZP4
SD (m) | 0.12 | 0.05 | 0.03
MAD (m) | 0.09 | 0.03 | 0.01
Mean (m) | 0.06 | 0.05 | 0.02
S3A_SR_2_LAN____20170304T162333_20170304T171402
Lead SSHA Jitter and Precision improves with Zero Padding sampling rates
Area of test track where we have consecutive Lead measurements
Lead SSHA (m)
ZP=2
ZP=4
No ZP
Notes: [macbook] cd /cpdata/SATS/RA/S3A/TDS/ZERO_PADDING_4_TDS/S3A_SR_2_LAN____20170304T162333_20170304T171402_20211026T172954_3029_015_083______LN3_O_NT_004.SEN3
/Users/alanmuir/software/cpom_software/cpom/altimetry/tools/plot_params_along_track.py -f zp4.nc -v sea_ice_ssha_20_ku_leads -m s3a -r 5340,5350 -f2 zp2.nc -f3 zp0.nc

## Slide 15
 | No ZP | ZP2 | ZP4
SD (m) | 0.12 | 0.06 | 0.04
MAD (m) | 0.11 | 0.04 | 0.02
Mean (m) | 0.10 | 0.05 | 0.03
S3A_SR_2_LAN____20170304T162333_20170304T171402
The effect of Zero-Padding (sampling rate) on Lead SSHA Jitter and Precision
Area of test track where we have consecutive Lead measurements
Lead SSHA (m)
No ZP
ZP=2
ZP=4
Notes: [macbook] cd /cpdata/SATS/RA/S3A/TDS/ZERO_PADDING_4_TDS/S3A_SR_2_LAN____20170304T162333_20170304T171402_20211026T172954_3029_015_083______LN3_O_NT_004.SEN3
/Users/alanmuir/software/cpom_software/cpom/altimetry/tools/plot_params_along_track.py -f zp4.nc -v sea_ice_ssha_20_ku_leads -m s3a -r 5340,5350 -f2 zp2.nc -f3 zp0.nc

## Slide 16
Measurement Accuracy over Sea Ice
Using available L2 data from <= PB 2.68
?
Sea ice floe
Lead
?

## Slide 18
To validate of S3A,B Freeboard measurements
Diagram adapted from Ricker, et al (AWI)
Comparison between snow, ice and radar freeboard requires knowledge of snow depth, density, temperature, snow properties, and surface roughness.
Validation Instrument/ Campaign | Radar Freeboard | Snow Freeboard | Ice Freeboard
Sentinel-3 | ✓ |  | 
CryoSat-2 | ✓ |  | 
ICESat-2 |  | ✓ | 
Operation IceBridge |  | ✓ | ✓ with snow radar
CryoVex Karen 20171 | ✓ | ✓ | 
Surface Measured
1 two under-flights of S3A over Fram Strait & Baffin Bay

## Slide 19
To validate of S3A,B Freeboard measurements
Diagram adapted from Ricker, et al (AWI)
Validation Instrument/ Campaign | Radar Freeboard | Snow Freeboard | Ice Freeboard
Sentinel-3 | ✓ |  | 
CryoSat-2 | ✓ |  | 
Surface Measured
CryoSat-2
S3A,B
As S3A,B and CryoSat-2
Similar Ku-band SAR altimeter instrument from (S3SRAL, CS2SIRAL)
Similar doppler footprint (~300m along track, by ~1.65km across track)
we expect a close match of freeboard measurement statistics in SAR mode with identical processing and appropriate calibration.
CryoSat-2 has 10 years of sea ice validation campaigns from which S3
can benefit from.

## Slide 20
S3A
CS2
Mean 25km Gridded Freeboard for March 2017

## Slide 21
S3A (IPF 6.18) and CS2 Baseline-D Gridded Mean Freeboard

## Slide 23
Mean Gridded ESA and GPOD S3AB and CS2 Freeboard (m) over Arctic (Winter 2019/2020)
Mean Gridded Freeboard (m)
Oct 2019
Dec 2019
Feb 2020
Mar 2020
Apr 2020
…
…
S3AB
Oct 2019
Dec 2019
Feb 2020
Mar 2020
Apr 2020
CS2
CS2
S3AB
4.9cm
S3AB GPOD
Monthly Changes in Mean Freeboard (Arctic, 2019/2020)
Notes: plot_fb_stats.py -a arctic_to_81_35N -v robust_mean -m s3as3b -c

## Slide 24
NSIDC Arctic area 10: Laptev Sea
Area of First Year Ice (FYI)
S3A
Dec 2019
S3B
CS2
S3AGPOD
Monthly Mean Freeboard : Laptev Sea
S3A
CS2
S3B
S3AGPOD
S3BGPOD
Dec 2019
Dec 2019
Dec 2019
Notes: ./plot_all_nsidc_arctic_areas.py -b nsidc_arctic_14 -m arctic

## Slide 25
NSIDC Arctic area 10: Central Arctic
Area of Multi Year Ice (MYI)
S3A
Dec 2019
S3B
CS2
S3AGPOD
Monthly Mean Freeboard : Central Arctic
S3A
CS2
S3B
S3AGPOD
S3BGPOD
Dec 2019
Dec 2019
Dec 2019
Notes: ./plot_all_nsidc_arctic_areas.py -b nsidc_arctic_14 -m arctic

## Slide 26
S3A
S3B
CS2
< 81.35N
Jan 2020
Jan 2020
Jan 2020
Mean Freeboard: Winter 2019/2020
CS2
S3A, S3B
SARin
NSIDC Basin 14: Canadian Islands
CS2 SARin
S3B
S3A
S3BG-POD
S3AG-POD
Notes: plot_fb_stats.py -a arctic_basin3 -v nvals -m s3a -s3b -cs2 -g
plot_fb_stats.py -a arctic_basin3 -v nvals -m s3a -s3b -cs2

## Slide 27
Gridded Freeboard Uncertainty
Using available L2 data from <= PB 2.68
?
25km
25km

## Slide 28
Gridded Freeboard Uncertainty
S3A
CS2

## Slide 29
Known L1b Issues (PB2.68)
# | Issue | Effect | Resolved in Thematic TDS
1 | No Hamming weighting in L1b | Hamming weighting dampens the contribution from high off-nadir beams to mitigate the effect of side-lobe ambiguities. This can result in contamination of echoes over floes with off-nadir leads. | ✓
2 | No Zero-padding in L1b | Under-sampled specular echoes over Leads : 3x loss of precision in lead SSHA, jitter | ✓ Sampling rate TBD

## Slide 31
L2 Sea Ice Evolutions/Tuning
# | Evolution/Tuning | Effect | In Thematic TDS
1 | Tuning of discrimination thresholds from OLCI imagery | Improved surface type discrimination: [Leads, Sea Ice Floes, Open Ocean, Unclassified] | ✓ [Will require re-tuning]
2 | Tuning of sea ice retracker bias following MSSL study | Improves the accuracy of the bias between floe and lead retrackers | ✓ [Will require re-tuning]
3 | Using Sea ice type in discrimination filtering (from instrument sea ice type parameter or daily OSI-SAF sea ice type ADF) as Tilling et al, 2018. | Allow improved filtering of ambiguous regions between MYI and FYI, as well as ice free and unclassified regions | x

## Slide 32: Lead/Floe Discrimination using S3 OLCI
S3 Discrimination Tuning Study
Discrimination with Current Thresholds
Discrimination with Retuned Thresholds
(Ocean and Land Colour Instrument)
lead peakiness: 21
floe peakiness: 11
lead SSD: n/a
floe SSD: n/a
lead peakiness: 24
floe peakiness: 16
lead SSD: 0.0027
floe SSD: 0.0033
Discrimination will require retuning for sea ice thematic products (Apr 2021)
(due to waveform shape changes)
Notes: Advantages of OLCI:
* Co-temporal to the altimetry data
- No need for ice drift vectors
* Removes the need to search for overlapping SAR images
- Currently the key issue with creating a large validation/tuning dataset
* Comes with rich header information
- Can help discard cloud cover
Cons
* Images have cloud cover, SAR doesn't
* Lower resolution than SAR
- Will get lead detections from small leads that appear to be floes
- However, this can still happen with SAR
* Primarily useful for daytime images
- Passive instrument whereas SAR is active

## Slide 33
L2 Sea Ice Evolutions/Tuning
# | Evolution/Tuning | Effect | In Thematic TDS
1 | Tuning of discrimination thresholds from OLCI imagery | Improved surface type discrimination: [Leads, Sea Ice Floes, Open Ocean, Unclassified] | ✓ [Will require re-tuning]
2 | Tuning of sea ice retracker bias following MSSL study | Improves the accuracy of the bias between floe and lead retrackers | ✓ [Will require re-tuning]
3 | Using Sea ice type in discrimination filtering (from instrument sea ice type parameter or daily OSI-SAF sea ice type ADF) as Tilling et al, 2018. | Allow improved filtering of ambiguous regions between MYI and FYI, as well as ice free and unclassified regions | x

## Slide 34
Sea Ice Retracker bias tuning (with PB2.68)

## Slide 35
L2 Sea Ice Evolutions/Tuning
# | Evolution/Tuning | Effect | In Thematic TDS
1 | Tuning of discrimination thresholds from OLCI imagery | Improved surface type discrimination: [Leads, Sea Ice Floes, Open Ocean, Unclassified] | ✓ [Will require re-tuning]
2 | Tuning of sea ice retracker bias following MSSL study | Improves the accuracy of the bias between floe and lead retrackers | ✓ [Will require re-tuning]
3 | Using Sea ice type in discrimination filtering (from instrument sea ice type parameter or daily OSI-SAF sea ice type ADF) as Tilling et al, 2018. | Allow improved filtering of ambiguous regions between MYI and FYI, as well as ice free and unclassified regions | x

## Slide 36
OSI SAF Global Sea Ice Type
  Daily product
Allows removal of ambiguous and
unclassified sea ice records.

## Slide 37
L2 Sea Ice Evolutions/Tuning
# | Evolution/Tuning | Effect | In Thematic TDS
4 | Snow Density: Use a linearly increasing snow density as per Mallet et al, 2020. | Currently a fixed mean arctic snow density of 400kg/m3 is used from Warren (99). As snow density increases during each Arctic season, Mallet et al recommends a linear seasonal increase of snow density: 𝜌𝑠 = 274.51 + 6.5t, where t represents the time in fractional month since October 15 | x
5 | New snow depth correction. Derivation and application of a dynamic snow depth correction using sea ice type, as is done for CS2 Baseline-E ‘snow_depth_cor_20_ku’ | Provide a correction to the calculated freeboard to account for the reduced propagation speed of light through the snow cover on sea ice floes | x (is in CS2 Baseline-E)

## Slide 38
L2 Sea Ice Evolutions/Tuning
# | Evolution/Tuning | Effect | In Thematic TDS
4 | Snow Density: Use a linearly increasing snow density as per Mallet et al, 2020. | Currently a fixed snow density of 400kg/m3 is used from Warren (99). As snow density increases during each Arctic season, Mallet et al recommends a linear seasonal increase of snow density: 𝜌𝑠 = 274.51 + 6.5t, where t represents the time in fractional month since October 15 | x
5 | New snow depth correction parameter. Derivation and application of a dynamic snow depth correction using sea ice type, as is done for CS2 Baseline-E ‘snow_depth_cor_20_ku’ | Provide a correction to the calculated freeboard to account for the reduced propagation speed of light through the snow cover on sea ice floes | x (is in CS2 Baseline-E)

## Slide 39
= snow depth
= speed of light through vacuum
= speed of light through snow
Correction is added to radar freeboard

## Slide 40
S3 Freeboard Performance (from PB2.68) Summary
Freeboard area extent matches monthly extent from passive microwave data in the Arctic.
Antarctica peak measurement numbers (Aug) lag behind peak extent (Sep/Oct) by ~1-2 months.
S3A and S3B coverage similar (orbits are different) and freeboard histogram shows no significant bias.
Precision of Lead SHA is ~3x worse than CryoSat (due to lack of ZP).
High freeboard variability near coastline compared to CryoSat (due to lack of ZP/Hamming).
~6cm freeboard bias as compared to CryoSat.
Much higher gridded monthly freeboard uncertainty than CryoSat.
Recommended next tuning/evolutions listed.
TN issued on Sea Ice Performance of PB2.68 (22-Oct-21)
Thematic Sea Ice TDS fixes most sea ice issues in PB2.68 (separate CM#8 presentation)