## Slide 1
Surface Elevation Change
Phase 2
1
1.
2.
Tom Slater2
Andrew Shepherd2, Inès Otosaka2, , Nitin Ravinder2,Alan Muir1 , Ben Palmer2
PM-03
Oct 2025
R&D Activities

## Slide 2
Surface Elevation Change
products produced from 34 years of Radar and Laser Altimetry
ERS-1
ERS-2
ENVISAT
CryoSat-2
Sentinel-3A
Sentinel-3B
1991
1996
2002
2010
2016
2018
ICESat-2
2025
radar altimetry
laser

## Slide 3
Overview of the Baseline Products

## Slide 4
Primary RA Parameters
Single Mission L2 Elevation
Backscatter

## Slide 5
5km
t0
tN
Surface change is modelled over time in each grid cell.
Local topography removed to leave the temporal change
Corrected for backscatter variations (correlated with elevation change) & GIA
Model-fit method of SEC Determination

## Slide 6
Surface Elevation Change (May 2016-Apr 2018)
Surface Elevation Change (May 2014-Apr 2016)
S3A
CryoSat-2
Pine Island Glacier
Pine Island Glacier
Thwaites Glacier
Thwaites Glacier
dh/dt
SEC
5km Grids
single mission dH timeseries ->
epoch average
140-days
->
dh/dt

## Slide 7
Single Mission Products : Main Parameters
Rignot(2016)

## Slide 8
Multi-mission SEC
5km Grids
Single Mission dH timeseries ->
Multi-mission RA
cross-calibration ->
5km Grid
5-year periods
monthly updates

## Slide 9
5-year Antarctic Ice Sheet Surface Elevation Change 2019-2024
2.0
1.5
1.0
0.5
0
-0.5
-1.0
-1.5
-2.0
m/yr
multi-mission radar altimetry
Multi- Mission dH timeseries ->
SEC
5km Grids

## Slide 10
Sensor Product | Grid Resolution | Temporal Coverage | Period | Main Parameters | Format
ERS-1 RA FDR4ALT v1 | 5km | 03-Aug-1991 02-Jun-1996 | 3 yrs, 10m | dh/dt, error | NetCDF + Quicklook jpg
ERS-2 RA FDR4ALT v1 | 5km | 13-May-1995 04-Jul-2003 | 8 yrs, 1m | dh/dt, error | NetCDF + Quicklook jpg
ENVISAT RA2 FDR4ALT v1 | 5km | 09-Apr-2002 18-Oct-2010 | 8 yrs, 5m | dh/dt, error | NetCDF + Quicklook jpg
CryoSat CryoTEMPO-D | 5km | 16-Jul-2010 31-Jun-2025 | 15 yrs, 0m | dh/dt, error | NetCDF + Quicklook jpg
Sentinel-3A BC04 | 5km | Dec-2016 31-Jun-2025 | 9 yrs, 7m | dh/dt, error | NetCDF + Quicklook pngs
Sentinel-3B BC04 | 5km | Nov-2018 31-Jun-2025 | 6 yrs, 8m | dh/dt, error | NetCDF + Quicklook pngs
Single RA Mission SEC Products
AIS CCI+ SEC Baseline Product Summary
Multi-mission
5-year means Monthly product 5km grid resolution dh/dt error new multi-mission cross-calibration algorithm developed
Multi-mission SEC

## Slide 11
R&D Activities in Phase-2

## Slide 12
R&D Activities in Phase-2
Integration and testing of new baseline products/formats for all RA Missions
Development of new SEC products from ICESat-2
Development of new Annual dH Products

## Slide 13
Integration of new Input Altimetry Products – (Phase-2)
Sensor | Products used in AIS CCI+ Phase-1 | New Product Baselines (AIS CCI phase-2, 2025)
ERS1 | REAPER v1 | FDR4ALT v1 Thematic Land Ice
ERS2 | REAPER v1 | FDR4ALT v1 Thematic Land Ice
ENVISAT | GDR v3 | FDR4ALT v1 Thematic Land Ice
CryoSat-2 | ESA L2i Baseline-D | ESA CryoTEMPO LI Baseline-D
Sentinel-3A | ESA L2 BC-04 | ESA Thematic Land Ice L2
Sentinel-3B | ESA L2 BC-04 | ESA Thematic Land Ice L2
New in phase-2: |  | 
ICESat-2 | - | ATL-06 v006, v007

## Slide 14
ICESat-2
2018 – 2025…
New SEC product in CCI phase-2
Required a new segmented processing scheme (due to higher data volume than RA)
Perform weighted surface fit using the IS2 uncertainty values as weighting
Method published:

## Slide 15
Weighted Surface Fitting
Elevation change for each grid cell is modelled using a plane fit method, using an uncertainty parameter as a model weight
Fragment gridded files
Divide gridded files into smaller fragments to reduce resource usage
Join fragments together
Rejoin fragments to recreate the whole target area
Masking and Gridding
Remove points that aren't in the target area and add remaining elevation measurements to a uniform grid
Epoch Averaging and Corrections
Apply glacial isostatic adjustment corrections if required, and calculate the mean elevation change within periods of a set length
Calculate dh/dt
Calculate the elevation change rate for the desired time period
ATL-06 Elevation data
ICESat-2 Laser Altimeter method

## Slide 16
ICESat-2
2018 – 2025…
New SEC product in CCI phase-2
Required a new segmented processing scheme (due to higher data volume than RA)
Perform weighted surface fit using the IS2 uncertainty values as weighting
Method published:
IS2 processing presentation by Nitin at PM1 (Sep 24).

## Slide 17
Antarctic Ice Sheet
Comparison of dH values vs ATL-15 and CS2

## Slide 18
East
West
Peninsula
Antarctic Ice Sheet
Comparison of dH values vs ATL-15 and CS2

## Slide 19: Annual Elevation Change (dH) grid product
Fill in the pole hole
Calculate dH per year
Interpolate missing cells
Calculate multi-mission time series

## Slide 20
AIS CCI phase-2 products will be
available shortly on a new portal

## Slide 21
ESACCI-AIS-L3C-SEC-CS2-5KM-20100927-20210202-fv1.zip
ESACCI-AIS-L3C-SEC-CS2-5KM-20100927-20210202-fv1.nc
+
ESACCI-AIS-L3C-SEC-CS2-5KM-20100927-20210202-fv1_sec.png
ESACCI-AIS-L3C-SEC-CS2-5KM-20100927-20210202-fv1_sec_uncertainty.png
ESACCI-AIS-L3C-SEC-CS2-5KM-20100927-20210202-fv1_basin_id.png
ESACCI-AIS-L3C-SEC-CS2-5KM-20100927-20210202-fv1_surface_type.png
Products Comply with CCI Data Standards v2.2
[Climate and Forecast Metadata ]CF 1.9 compliant

## Slide 22
Phase-2 SEC Summary
Integration of all new L2 product baselines for all RA missions
  ERS-1, ERS-2,ENVISAT, CS2, S3A, S3B
Development of new products for Phase-2
  ICESat-2
    new processing chain developed at NU using method as per Ravinder at al, GRL, 2024
  Annual DEMs from full RA timeframe
  Final phase-2 product verification & validation in process
  New product portal will be available in Q4 2025 for product dissemination and basin time series visualization.